FACULTY OF ENGINEERING TECHNOLOGY

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

HYDRAULICS AND HYDROLOGY LABORATORY

LABORATORY INSTRUCTION SHEETS

| COURSE CODE | BNP 20103 |
| --- | --- |
| EXPERIMENT NO. | 1 |
| EXPERIMENT TITLE | INFILTRATION TEST |
| DATE |  |
| GROUP NO. |  |
| LECTURER/ INSTRUCTOR/ TUTOR | 1) |
|  | 2) |
| DATE OF REPORT SUBMISSION |  |
| DISTRIBUTION OF MARKS FOR LABORATORY REPORT | ATTENDANCE/PARTICIPATION/DISPLINE | /5% |
|  | INTRODUCTION: | /5% |
|  | PROCEDURE: | /5% |
|  | RESULTS & CALCULATIONS | /15% |
|  | ANALYSIS | /15% |
|  | DISCUSSIONS: | /20% |
|  | ADDITIONAL QUESTIONS: | /15% |
|  | CONCLUSION: | /10% |
|  | SUGGESTION & RECOMENDATIONS | /5% |
|  | REFERENCES: | /5% |
|  | TOTAL: | /100% |
| EXAMINER COMMENTS: | RECEIVED DATE AND STAMP |

STUDENT CODE OF ETHICS

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

FACULTY OF ENGINEERING TECHNOLOGY

I hereby declare that I have prepared this report with my own efforts. I also admit to not accept or provide any assistance in preparing this report and anything that is in it is true.

- Group Leader               __________________________________________(Signature)

Name            :              __________________________________

Matrix No.    :               __________________________________

- Group Member 1          __________________________________________(Signature)

Name           :               __________________________________

Matrix No    :               ___________________________________

- Group Member 2          __________________________________________(Signature)

Name          :                __________________________________

Matrix No.   :                __________________________________

| OBJECTIVE To identify the characteristics of the infiltration rate of water into soils in the field. . |
| --- |
| LEARNING OUTCOMES At the end of the course, students should be able to apply the knowledge and skills they have learned to: a. Understand the concept of infiltration of water into soils. b. Understand the factors which influence the infiltration rates. |
| INTRODUCTION / THEORY The volume of water used during each measured time interval is converted into an incremental infiltration velocity for both the inner ring and annular space using the following equations; where, is the inner ring incremental infiltration velocity(cm/hr), is the volume of water used during time interval to maintain constant head in the inner ring (mL), is the internal area of inner ring (cm2) and is the time interval (hour). For the annular space between rings, calculate as follows; where is the annular space incremental infiltration velocity (cm/hr), is the volume of water used during time interval to maintain constant head in the annular space between the rings (mL), is the area of annular space (cm2) and is the time interval (hour). The infiltration rate calculated with the inner ring should be the value used for results if the rates for the inner ring and annular space differ. The difference in rates is due to divergent flow. |
| EQUIPMENTS Two stainless steels rings measure 12” and 24” diameter x 20” high Marriotte tube |
| PROCEDURES After a test site has been selected and the soil surfafe has been prepared, the outer. Ring is driven into the soil using s driving cap on the top which a wood block can be used to absorb the blow from a sledge hammer. The outer ring is inserted by moving the wood block araound the edge of the driving cap. The ring is inserted to a depth that will (a) prevent the test water from leaking to the ground surface surrounding the ring, and (b) be deeper than the depth to which the innner ring will be driven. A depth of about 15cm is usually adequate. Once the outer ring is in place, the inner ring can be centered inside the large ring and driven to a depth that will prevent leakage of water the ground surface surrounding the ring. A depth of about 5-10 cm is usually adequate. Both the outer and the innner ring should be level. The soil surrounding the wall of the ring (s) should be exempt of excessive disturbance. In case extensive carcking or heave are observed, the ring (s) should be reset to a different location using a technique that will minimize such disturbance. There are three ways to maintain constant head (water lever) within the inner ring and annular space between the two ring, manually controlling the flow liquid, the use of constant – level float valves, or the use of a mariotte tube. The latter option is the preferred one since it auto-regulates water flow to the ring. A pair or water bottle is used to fill both rings with water to the same desired depth in each ring. The water flow from the mariotte tube can than be initiated. As soon as the fluid level becomes constant, the water level in the inner ring and in the annular space is measure (and recorded) to the nearest 2mm using a ruler or a tape measure. The water level is maintained at a selected head (level) in both the inner ring annular space between rings throughout the test to prevent flow of water from one ring to the other. The volume of water that is added to maintain a constant head in the inner ring. And annular space during each timing interval is determined by measuring the change in elevation of the water level in the appropriate graduated mariotte tube. For average soils, the volume of water used to maintain the head recorded at every 5 min intervals for at least 6 hours, or until a relatively costant infiltration rate is achieved. The appropriate reading frenquency may be determined only through experience and may be more frenquet for high-K meterials |
| RESULTS AND CALCULATIONS TABLE 6.1 Infiltration rate experiment results Time, t (s) Inner (mm) Infiltration Capacity (mm) Infiltration Rate (mm/s) *Stop after 3 constant readings |
| QUESTIONS Plot a graphs of: Infiltration capacity versus time Infiltration rate versus time From the graph in 7.1(a), please identify the basic of infiltration rate Sketch a graphs of infiltration rate versus time for the three different characteristics soils: Dry soil Wet soil Saturated soil Explain each of the graphs |
| Prepared by / Disediakan oleh: Signature/Tandatangan: Name/Nama: DR. NOR HASLINA HASHIM Date/Tarikh : SEPTEMBER 2014 | Approved by / Disahkan oleh : Signature / Tandatangan : Name / Nama : ASSOC. PROF. DR. ISHAK BABA Date / Tarikh :2 SEPTEMBER 2014 |