FACULTY OF ENGINEERING TECHNOLOGY

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

HYDRAULICS AND HYDROLOGY LABORATORY

LABORATORY INSTRUCTION SHEETS

| COURSE CODE | BNP 20103 |
| --- | --- |
| EXPERIMENT NO. | 3 |
| EXPERIMENT TITLE | OPEN CHANNEL (HYDRAULIC JUMPS) |
| DATE |  |
| GROUP NO. |  |
| LECTURER/ INSTRUCTOR/ TUTOR | 1) |
|  | 2) |
| DATE OF REPORT SUBMISSION |  |
| DISTRIBUTION OF MARKS FOR LABORATORY REPORT | ATTENDANCE/PARTICIPATION/DISPLINE | /5% |
|  | INTRODUCTION: | /5% |
|  | PROCEDURE: | /5% |
|  | RESULTS & CALCULATIONS | /15% |
|  | ANALYSIS | /15% |
|  | DISCUSSIONS: | /20% |
|  | ADDITIONAL QUESTIONS: | /15% |
|  | CONCLUSION: | /10% |
|  | SUGGESTION & RECOMENDATIONS | /5% |
|  | REFERENCES: | /5% |
|  | TOTAL: | /100% |
| EXAMINER COMMENTS: | RECEIVED DATE AND STAMP |

STUDENT CODE OF ETHICS

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

FACULTY OF ENGINEERING TECHNOLOGY

I hereby declare that I have prepared this report with my own efforts. I also admit to not accept or provide any assistance in preparing this report and anything that is in it is true.

- Group Leader               __________________________________________(Signature)

Name            :              __________________________________

Matrix No.    :               __________________________________

- Group Member 1          __________________________________________(Signature)

Name           :               __________________________________

Matrix No    :               ___________________________________

- Group Member 2          __________________________________________(Signature)

Name          :                __________________________________

Matrix No.   :                __________________________________

| OBJECTIVE To investigate the characteristic a standing wave (the hydraulic jump) produced when waters beneath an undershot weir and to observe the flow patterns obtained. |
| --- |
| LEARNING OUTCOMES At the end of the course, students should be able to apply the knowledge and skills they have learned to: a. Understand the concept and characteristics of hydraulic jump. b. Understand the factors which influence the hydraulic jump. |
| INTRODUCTION / THEORY When water flowing rapidly changes to slower tranquil flow, a hydraulic jump or standing wave is produced. This phenomenon can be seen where water shooting under a sluice gate mixes with deeper water downstream. It occurs when a depth less than critical changes to a depth which is greater than critical and must be accompanied by loss of energy. An undular jump occurs when the change in depth is small. The surface of the water undulates in a series of oscillations, which gradually decay to a region of smooth tranquil flow. A direct jump occurs when the change in depth is great. The large amount of energy loss produces a zone of extremely turbulent water before it settles to smooth tranquil flow. By considering the forces acting within the fluid on either side of a hydraulic jump of unit width it can be shown that: |
| Where, is the total head loss across jump (energy dissipated) (m), is the mean velocity before jump (m/s), is the depth of flow before hydraulic jump (m), is the mean velocity after hydraulic jump (m) and is the depth of flow after hydraulic jump (m). Because the working section is short, and . Therefore, simplifying the above equation, |
| EQUIPMENTS Self-contained Glass Sided Tilting Flume Adjustable undershot weir Instrument carrier Hook and point gauge |
| PROCEDURES Ensure the flume is level, with the downstream tilting overshot weir, E at the bottom of its travel. Measure and record the actual breadth b (m) of the undershot weir. Install the undershot weir towards the inlet end of the flume and ensure that it is securely clamped in position. Adjust the undershot weir to position the sharp edge of the weir 20 mm above the bed of the channel. Increase the height of the tilting overshot weir until the downstream level just start to rise. Gradually open the flow control valve and adjust the flow (Q < 0.013 m3/s) until an undular jump is created with small ripple decaying towards the discharge end of the working section. Observe and sketch the flow pattern. Increase the height of water upstream of the undershot weir by increasing the flow rate and increase the height of the tilting overshot weir to create a hydraulic jump in the centre of the working section. Observe and sketch the flow pattern. Measure and record the values of d1,d3,dg and q . Repeat this for other flow rates (upstream head) and heights of the gate . |
| RESULTS AND CALCULATIONS Calculate v1 and plot dg against v1 Calculate /d1 and plot /d1 against d3/d1 Calculate dc and verify d1 <dc < d3 Channel width, b =……………..m Weir Opening dg (m) Upstream Flow Depth do (m) Flow Depth Above Jump d1 (m) Flow Depth Below Jump d3 (m) Flow Rate Q (m3/s) v1 |
| QUESTIONS Verify the force of the stream on either side of the jump is the same and that the specific energy curve predicts a loss equal to. Suggest application where the loss of energy in hydraulic jump would be desirable. How is the energy dissipated? |
| Prepared by / Disediakan oleh: Signature/Tandatangan Name/Nama: DR. NOR HASLINA HASHIM Date/Tarikh : SEPTEMBER 2014 | Approved by / Disahkan oleh : Signature / Tandatangan : Name / Nama : ASSOC. PROF. DR. ISHAK BABA Date / Tarikh : SEPTEMBER 2014 |