FACULTY OF ENGINEERING TECHNOLOGY

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

HYDRAULICS AND HYDROLOGY LABORATORY

LABORATORY INSTRUCTION SHEETS

| COURSE CODE | BNP 20103 |
| --- | --- |
| EXPERIMENT NO. | 4 |
| EXPERIMENT TITLE | PELTON TURBINE |
| DATE |  |
| GROUP NO. |  |
| LECTURER/ INSTRUCTOR/ TUTOR | 1) |
|  | 2) |
| DATE OF REPORT SUBMISSION |  |
| DISTRIBUTION OF MARKS FOR LABORATORY REPORT | ATTENDANCE/PARTICIPATION/DISPLINE | /5% |
|  | INTRODUCTION: | /5% |
|  | PROCEDURE: | /5% |
|  | RESULTS & CALCULATIONS | /15% |
|  | ANALYSIS | /15% |
|  | DISCUSSIONS: | /20% |
|  | ADDITIONAL QUESTIONS: | /15% |
|  | CONCLUSION: | /10% |
|  | SUGGESTION & RECOMENDATIONS | /5% |
|  | REFERENCES: | /5% |
|  | TOTAL: | /100% |
| EXAMINER COMMENTS: | RECEIVED DATE AND STAMP |

STUDENT CODE OF ETHICS

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

FACULTY OF ENGINEERING TECHNOLOGY

I hereby declare that I have prepared this report with my own efforts. I also admit to not accept or provide any assistance in preparing this report and anything that is in it is true.

- Group Leader               __________________________________________(Signature)

Name            :              __________________________________

Matrix No.    :               __________________________________

- Group Member 1          __________________________________________(Signature)

Name           :               __________________________________

Matrix No    :               ___________________________________

- Group Member 2          __________________________________________(Signature)

Name          :                __________________________________

Matrix No.   :                __________________________________

| OBJECTIVE To determine the characteristics of Pelton Turbine operation by using several speed. |
| --- |
| LEARNING OUTCOMES At the end of the course, students should be able to apply the knowledge and skills they have learned to: a. Understand the basic operating system of the Pelton turbine. b. Understand the factors which influence the efficiency of turbine. |
| INTRODUCTION / THEORY A Pelton Turbine characteristic operation curve can be derived by using the same method as a pump. It is because the velocity is usually assumed as an independent parameter when the plotting of power, efficiency, torque and discharge are carried out. Mechanical Power, Pm (watt) = Rotation (, Nm) x Circular velocity ( , rad/sec). Where, T=Force(N) Radius(m)(Nm) and (rad/s) where, 1 revolution is equal to 2radius. Meanwhile, Water Power, where, is water density (100kg/m3),is gravity constant (9.81m/s2), is head at inlet point (m) and is flowrate (m3/s). Wheel efficiency, . To convert the unit of ‘rpm’ to ‘radians per minute’ is given by, rpm=( revolution/min)=( x 2radian)/min. |
| EQUIPMENTS Pelton turbine Tachometer Stop watch |
| PROCEDURES Put the Pelton turbine equipment on the hydraulic bench and connect it to the water supply by using the provided connecter. Tighten the optic tachometer by using clip. Then, make sure that the turbine drum is free from any load (0.0N). Fully open the valve controller. Then, level the tachometer until the rotation reaches the maximum value of 2000 rotation/minute or rpm. Records the reading of tachometer, flow rate, pressure at inlet point (H) and load, W2 (N). Put the brake equipment on the turbine drum. Then, level the brake on the right spring at W1. Start with the W1 = 1.0N. Record all the readings in the Table 6.1. Repeat 3-6 with W varies in the range of 1.5N to 6.0N. |
| RESULTS AND CALCULATIONS TABLE 6.1 Results of Pelton Turbine experiment RPM (rad/s) W1 (N) 0 1.0 1.5 2.0 2.5 3.0 3.5 4.0 4.5 5.0 5.5 6.0 W2 (N) W2 –W1 (N) Drum Radius x10-3m 30 30 30 30 30 30 30 30 30 30 30 30 Rotation (Nm) Pm(W) Volume (l) Volume (m³) Time(s) Flowrate (m3/s) Pressure (mH2O) Pw (W) Efficiency (%) Drum brake radius on turbine (DBR) = 30 x 10-6 (m) Total Force = (W2-W1) = …………….(Fixed W1, reading for each starting load) Rotation, = …………….(rad/s) Mechanical Power, Pm = ………………(Watt) Water Power, Pw = ………………..(Watt) Efficiency, =……………… (%) |
| QUESTIONS Plot graph of: the rotation power curve efficiency curve discharge versus motor speed Give a comment on the graph obtained Calculate the velocity where the maximum power is reached. Give your comment based on the level of maximum efficiency. State five (5) safety factors that have been taken in the experiment? |
| Prepared by / Disahkan oleh: Signature/Tandatangan: Name/Nama: DR. NOR HASLINA HASHIM Date/Tarikh : SEPTEMBER 2014 | Approved by / Disahkan oleh : Signature / Tandatangan : Name / Nama : DR. NOR HASLINA HASHIM Date / Tarikh : SEPTEMBER 2014 |