FACULTY OF ENGINEERING TECHNOLOGY

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

HYDRAULICS AND HYDROLOGY LABORATORY

LABORATORY INSTRUCTION SHEETS

| COURSE CODE | BNP 20103 |
| --- | --- |
| EXPERIMENT NO. | 5 |
| EXPERIMENT TITLE | FRANCIS TURBINE |
| DATE |  |
| GROUP NO. |  |
| LECTURER/ INSTRUCTOR/ TUTOR | 1) |
|  | 2) |
| DATE OF REPORT SUBMISSION |  |
| DISTRIBUTION OF MARKS FOR LABORATORY REPORT | ATTENDANCE/PARTICIPATION/DISPLINE | /5% |
|  | INTRODUCTION: | /5% |
|  | PROCEDURE: | /5% |
|  | RESULTS & CALCULATIONS | /15% |
|  | ANALYSIS | /15% |
|  | DISCUSSIONS: | /20% |
|  | ADDITIONAL QUESTIONS: | /15% |
|  | CONCLUSION: | /10% |
|  | SUGGESTION & RECOMENDATIONS | /5% |
|  | REFERENCES: | /5% |
|  | TOTAL: | /100% |
| EXAMINER COMMENTS: | RECEIVED DATE AND STAMP |

STUDENT CODE OF ETHICS

DEPARTMENT OF CIVIL ENGINEERING TECHNOLOGY

FACULTY OF ENGINEERING TECHNOLOGY

I hereby declare that I have prepared this report with my own efforts. I also admit to not accept or provide any assistance in preparing this report and anything that is in it is true.

- Group Leader               __________________________________________(Signature)

Name            :              __________________________________

Matrix No.    :               __________________________________

- Group Member 1          __________________________________________(Signature)

Name           :               __________________________________

Matrix No    :               ___________________________________

- Group Member 2          __________________________________________(Signature)

Name          :                __________________________________

Matrix No.   :                __________________________________

| OBJECTIVE To determine the relationship between the head, flow rate, velocity, power and efficiency of Francis Turbine. |
| --- |
| LEARNING OUTCOMES At the end of the course, students should be able to apply the knowledge and skills they have learned to: a. Understand the basic operating system of the Francis Turbine. b. Understand on the factors which influence the efficiency of turbine. |
| INTRODUCTION / THEORY Hydraulic power can be obtain at the turbine inlet (usually known in watt unit) and can be calculated as,, and Q as the volume discharge that can be read from the measuring equipment (m3/s) and is a water weight per unit of volume (9820 N / m3). is a total head (m) which can be calculated (using theorem Bernoulli method) in a circuit section flow just before the turbine in a location of pressure head as a total of three parameter, which is Hman is a the differences of pressure head position which measured the pressure and the turbine shaft bar. As using the experimental table, (if the pressure decreasing at the turbine point out which cause by the mixer which count as an available head, Hman can be calculated as the height differences between the pressure gauging point position and the point of water level at the outflow of reservoir) is a kinetic parameter which cause by water velocity, vm (in m / s), at the pressure gauging location, where the pipe section is Sm (this value is not S and v value at the inlet section). , where as g is the gravity constant (9.81m/s2) and vm=Q/Sm. is a resultant parameter from water pressure, (in unit N / m2) as measured by pressure gauging. In calculation table, the readable gauging value which has been read by four gauging, all the readable value from the calculation can be added by the related values, vm, Hman, Hkin, Hpres, Htot, Phyd, where as , is the turbine angular velocity (in rad/s), n is a turbine average velocity obtain by reader equipment (RPM) and c is a braking torque |
| velocity at the turbine shaft as obtain by reader equipment (Nm). Lastly, the turbine overall efficiency, is calculated as the ratio of power at outlet point compared to the generated power. Last table arrangement for the experimental value and the calculation value (for each z) can be explained in a provided table. |
| EQUIPMENTS Francis Turbine equipment |
| PROCEDURES Close the delivery control shutter. Fixed the distributor leverage at the chosen value ( 50% and 100%). Open the delivery control shutter until desired flow rate. Records the reading of pressure (), speed (), flow rate (), and voltage (V) for each distributor leverage value in Table 6.1. Repeat 3-4 steps with different distributor leverage value. PRECAUTION: Must ensure the delivery control shutter should be closed before switch on the equipment. Carelessness may cause equipment damage. |
| RESULTS AND CALCULATIONS (REFER TO APPENDIX A) |
| QUESTIONS Plot a graph of: Turbine velocity versus flow rate. Turbine velocity versus output torque. Turbine velocity versus hydraulic power. Turbine velocity versus mechanical power. Turbine velocity versus efficiency. Give your comment(s) from the graph obtained. State five (5) safety factors that have been taken in the experiment |
| Prepared by / Disahkan oleh: Signature/Tandatangan: Name/Nama: DR. NOR HASLINA HASHIM Date/Tarikh : SEPTEMBER 2014 | Approved by / Disahkan oleh : Signature / Tandatangan : Name / Nama : ASSOC. PROF. DR. ISHAK BABA Date / Tarikh : SEPTEMBR 2014 |

APPENDIX A

Table 6.1: Francis Turbine Experimental Data

| z (%) | Pressure, Pm (bar) | Flowrate, Q (m3/h) | Speed, n (RPM) | Voltage, V (volt) | Current Reading, I (ampere) | Current Reading, I (%) | Average of Pressure, Pm (bar) | Average of Flowrate, Q (m3/h) | Average of Speed, n (RPM) | Average of Voltage, V (volt) | Average of Ampere, I (ampere) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 50% |  |  |  |  |  |  |  |  |  |  |  |
| 100% |  |  |  |  |  |  |  |  |  |  |  |

CONTINUED

| z (%) | Electrical Power, Pel (W) | Pipe Cross Section, Sm (m2) | Water Speed, Vm (m/s) | Distance Between Turbine Shaft & Pressure Tap, Hman (m) | Kinetic, Hkin (m) | Pressure, Hpres (m) | Total Head, Htot (m) | Mechanical Power, Pm (watt) | Hydraulic Power, Phyd (watt) | Efficiency, Pm/Phyd (watt) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 50% |  |  |  |  |  |  |  |  |  |  |
| 100% |  |  |  |  |  |  |  |  |  |  |